An I2C protocol is one of the serial communication protocol that is used for the chip to chip communication. Similar to the I2C protocol, SPI and UART also used for the chip to chip communication.
The I2C is the short form of Inter-Integrated Circuit, is a type of bus, which designed and developed by Philips in 1980 for inter-chip communication.I2C is adopted by a lot of vendor companies for the chip to chip communication.
It is a multi-master and multi-slave serial communication protocol means that we have the freedom to attach multiple IC at a time with the same bus. In I2C protocol, communication always started by the master and in the case of multi-master, only one master has the ownership of the bus.
In this article, you will learn the I2C protocol and its bus configuration and uses in the chip to chip communication.

### What is I2C?
I2C is a serial communication protocol. It provides the good support to the slow devices, for example, EEPROM, ADC, and RTC etc.
I2c is not only used with the single board but also used with the other external components which have connected with boards through the cables.
I2C is basically two-wire communication protocol.It uses only two wire for the communication. In which one wire is used for the data (SDA) and other wire is used for the clock (SCL).
In I2C, both buses are bidirectional, which means master able to send and receive the data from the slave. The clock bus is controlled by the master but in some situations slave is also able to suppress the clock signal, but we will discuss it later.
Additionally, an I2C bus is used in the various control architecture, for example, SMBus (System Management Bus), PMBus (Power Management Bus), IPMI (Intelligent Platform Management Interface) etc.

### Why use I2C
Unlike the serial com port I2c is the synchronous communication, in I2C both master and slave use the shared clock which is produced by the master.
In serial port, both the transmitter and receiver device have own clock generator. Hence it is very important to minimize the difference between the clock of the transmitter and slave otherwise data will be corrupt during the communication.
Another disadvantage of asynchronous serial com port is that only two devices transmit and receive the data but beside it, I2C can be multi-master and multi-slave.
Asynchronous serial is used a UART chip for the communication.
There is no specific limit defined for the asynchronous communication but most of the serial devices support up to the maximum baud rate 230400 (bits per second).
SPI is full duplex and faster than I2c Although sometimes I2C is much easier and beneficial. In I2C, we needed only two wire for the communication but in SPI we have needed four wire for the communication.I2c can be multi-master but SPI never can be multi-master.