## Slide 1
Video Basics
Ron Birkett Technical Training Instructor

## Slide 2
Do you want to build something like this…
PDA
PVR
TV Cell Phone
Security Camera
DVD-R
Portable DVD
Digital Video Cameras
Broadband Set Top Box
Media Encoders/Decoders
Digital Still Cameras
Notes: Each of these carry of TI's Video Decoder Chips.
TVP5150A - PDA, Portable DVD, TV Cell Phone, Security Camera
TVP5146 - LCD TV, DVD Player, DLP, PVR

## Slide 3: Which works best for your needs?
12 times the size … Is it twelve times the quality?
358 x 238 pixels
23 KB
1491 x 991 pixels
303 KB
What resolution should you use?
Printers or displays with fixed dot (or pixel) densities might lead you to a specific resolution
Conforming to a specific standard (NTSC, PAL, etc.) might dictate your choice
Data rate, processing rate, storage capacity may direct your decision
Notes: Would it be ideal to have Infinite Resolution?
  Eye can see about 1800 DPI (very subjective figure)
  Storage and transmission costs  with higher resolution
  Often, it pays to capture at higher resolution so that after editing and cropping, image is not overly degraded

## Slide 4: How about between these?
How about now
358 x 238 pixels
23 KB
? x ? pixels
? KB

## Slide 5: Which works best for your needs?
12 times the size … Is it twelve times the quality?
358 x 238 pixels
23 KB
1491 x 991 pixels
303 KB
What resolution should you use?
  For printers or displays with fixed dot (or pixel) densities, this might lead you to a particular resolution
Notes: Would it be ideal to have Infinite Resolution?
  Eye can see about 1800 DPI (very subjective figure)
  Storage and transmission costs  with higher resolution
  Often, it pays to capture at higher resolution so that after editing and cropping, image is not overly degraded

## Slide 6: Resolution
Perceived resolution is a function of:
  Actual resolution
  Distance
  Size of diplay (i.e. size of pixels)

## Slide 7: Various Standard Resolutions
Format | Application(s) | NTSC | PAL
D1 | Full Analog Television Resolution | 720 x 480 | 720 x 576
SIF | Resolution VHS VCR is capable of | 352 x 240 | 352 x 288
ATSC | Digital Television | 18 different resolutions/rates (three most common are shown) | 
 | Standard Definition (SDTV) | 720 x 480 | 
 | High Definition (HDTV) | 1280 x 720 1920 x 1080 | 
4CIF | Often used in Video Conferencing or for small screen applications (specified for various codecs, e.g. H.261) | 704 x 576 352 x 288 176 x 144 | 
CIF |  |  | 
QCIF |  |  | 

## Slide 8: Various Standard Resolutions
Format | Application(s) | NTSC | PAL
D1 | Full Analog Television Resolution | 720 x 480 | 720 x 576
SIF | Resolution VHS VCR is capable of | 352 x 240 | 352 x 288
ATSC | Digital Television | 18 different resolutions/rates (three most common are shown) | 
 | Standard Definition (SDTV) | 720 x 480 | 
 | High Definition (HDTV) | 1280 x 720 1920 x 1080 | 
4CIF | Often used in Video Conferencing or for small screen applications (specified for various codecs, e.g. H.261) | 704 x 576 352 x 288 176 x 144 | 
CIF |  |  | 
QCIF |  |  | 
NTSC National Television Standards Committee TV format in North America, Japan and much of the world
PAL Phase Alternation Line TV format for Europe (and more of the world)
SECAM Sequentiel Couleur Avec Memoire TV format for France (and a couple others)
ATSC Advanced Television Systems Committee Digital TV standards (including HDTV)
D1 Standard Digital Videotape Format Often used to denote full standard TV resolution
CIF Common Interface Format or Common Interchange Format

## Slide 9: How is NTSC "D1" Resolution Defined?

## Slide 10: Which Video Clip Looks Better?
5 frames/sec
15 frames/sec

## Slide 11: Which Video Clip Looks Better?
Same data rate between these two
progressive
15 frames/sec
interlaced
30 fields/sec

## Slide 12: Progressive and Interlaced
Interlaced formats decrease the data rate by eliminating every other line
  Each set of odd or even lines are called a field:
    Field 1: Odd lines are "painted" every 1/60th of a second
    Field 2: Even lines are painted the next 1/60th of a second
  In the end, the two fields end up "painting" the entire screen 30 times/second
Conversely, progressive formats scan (i.e. paint) the entire screen in one pass
  Each full screen scan is called a frame
  Frames are commonly updated at 25, 29.97, 30, or 60 frames per second (fps)
Notes: Interlacing is visible in movies which have a height > 288 (NTSC: > 240). So when you capture a movie, say, 384x288 or smaller you won't see interlaced frames. It's practically blending. Some capture cards don't blend but drop every second field with sizes smaller or equal to 288.

## Slide 13: Interlacing Side Effects
While interlacing can reduce the data rate without reducing the image resolution, it does produce some side effects
Tomato is moving right in this example
See how the image is distorted due to movement between the two fields …
This is called "combing" (or "feathering)
Similarly the skier seems to flicker (called "line twitter")
Worse yet, very thin image elements (such as the ski pole) that are only one line wide seem to disappear and reappear (exacerbated by vertical movement)
As long as nothing in the picture changes (such as when showing a still image), the alternating fields will actually complement each other and form a complete picture. The display will flicker and scan lines will be visible (both a inherent of an interlaced system), but that's life in an interlaced world. We don't spend the evening looking at a still picture on the TV though. The moment something moves, we get interlacing artifacts! 1

## Slide 14: NTSC, PAL, and CIF Formats
NTSC | Resolution | Frame Rate | I/P | Data Rate
D1 | 720 x 480 | 59.94 fields/sec | I | 10M pix/sec
SIF | 352 x 240 |  |  | 5M pix/sec
PAL | Resolution | Frame Rate | I/P | Data Rate
D1 | 720 x 576 | 50 fields/sec | I | 10M pix/sec
SIF | 352 x 288 |  |  | 5M pix/sec
4CIF | 704 x 576 | 30 frames/sec | P | 12M pix/sec
CIF | 352 x 288 | 30 frames/sec | P | 3M pix/sec
QCIF | 176 x 144 | 30 frames/sec | P | 760K pix/sec
Scan Method in Table Above
  I = Interlaced
  P = Progressive
Notice how the data rate is the same between NTSC and PAL, even though the resolution and frame rates are different
Notes: Data Rate
10,357,632 p/sec
5,178,816 p/sec
Data Rate
10,368,000 p/sec
5184000 p/sec

## Slide 15: ATSC Formats
ATSC | Name | Resolution | Frame Rate (per second) | I/P | Data Rate (pixels/sec)
SDTV | 480i | 720 x 480 | 60 fields | I | 10 M
 | 480p | 720 x 480 | 60 frames | P | 20 M
HDTV | 720p | 1280 x 720 | 60 frames | P | 55 M
 | 1080i | 1920 x 1080 | 60 fields | I | 62 M
 | 1080p | 1920 x 1080 | 60 frames | P | 124 M
Key
  SDTV = Standard Definition Television
  HDTV = High Definition Television
  I = Interlaced
  P = Progressive
Standard supports both NTSC rates and integer rates: i.e. 60.00, 59.94, 30.00, 29.97, 24.00, and 23.98
Notice the similarity between 720p and 1080i data rates
  Debate solved between competing HD formats by including both
  In USA, of four major broadcast networks, two chose 720p while the other two chose 1080i
  ATSC compatible HDTV's provide one native format (720p, 1080i), but they must convert the other so they can display both
Notes: Data Rate
10,357,632 p/sec
5,178,816 p/sec
Data Rate
10,368,000 p/sec
5184000 p/sec

## Slide 16: Color Depth
1-bit/pixel = black/white
8-bits/pixel = 256 greys
4-bits/pixel = 16 colors
8-bits/pixel = 256 colors
8-bits Red
8-bits Green
8-bits Blue
24-bits/pixel = 16 million colors

## Slide 17: RGB Color
8-bits Red
8-bits Green
8-bits Blue
All color can be composed by adding specific amounts of R, G, & B
8-bits (28) specifies the amount of each color
This is the scheme used by most electronic displays to generate color; e.g. we often call our computer monitors, "RGB displays"
0 255

## Slide 18: Color Reduction
Human eye is not as sensitive to color as it is to Luminance
dark
vs
light
To this end, to save costs the various standards decided to:
  Maintain luminance information in our images, but
  Reduce color information
Using RBG, though, how do we easily reduce color information without removing luminance?
For this, and other technical reasons, a separate color space was chosen by most video standards …

## Slide 19: Color Spaces
18
-37
20
98
100
31
32
24
81
248
70
32
23
Y:
Cb:
Cr:
Color Spaces:
  Along with RGB, there are many different ways to represent color
  This "picker" example demonstrates 4 different common color spaces

## Slide 20: Color Spaces
18
-37
20
98
100
31
32
24
81
248
70
32
23
Y:
Cb:
Cr:
Color Spaces:
  Along with RGB, there are many different ways to represent color
  This "picker" example demonstrates 4 different common color spaces
YCbCr is the color space most often used in video, where:
  Y = Luminance (Black/White/Gray)
  Cb = Blue difference value (Y – Blue)
  Cr = Red difference value (Y – Red)
Notes: *The human eye is able to see millions of colors, but it may be difficult to see the difference in colors that are very similar. Usually holding one shade up to another is the only way to really see the difference.

## Slide 21: What is YCbCr?
Video
Source
Y
Cb
Cr
Y
Cb
Cr
R
G
B
Even though most displays actually use RGB create the image, YCbCr is used most often in consumer electronics for transmission of the image
Historically, B/W televisions transmitted only luminance (Y)
The color signals were added later

## Slide 22: YCbCr  YPbPr
Y
Cb
Cr
Video DAC
(e.g. Encoder)
Y
Pb
Pr
When YCbCr values are converted to analog signals, they are called YPbPr

## Slide 23: YCbCr  YPbPr
Y
Cb
Cr
Y
Cb
Cr
Y
Cb
Cr
Y
Cb
Cr
…
Video DAC
(e.g. Encoder)
Memory
Y
Pb
Pr
When YCbCr values are converted to analog signals, they are called YPbPr
Digital displays sample the signals to regain the discrete values

## Slide 24: Packed Pixel (Interleaved)
Y
Cb
Cr
Y
Cb
Cr
Y
Cb
Cr
Y
Cb
Cr
…
Video DAC
(e.g. Encoder)
Memory
Y
Pb
Pr
When YCbCr values are converted to analog signals, they are called YPbPr
Digital displays sample the signals to regain the discrete values
In memory, pixel values can be:
  Packed (i.e. interleaved)
  Sorted (shown on next slide)

## Slide 25: Packed Pixel (Sorted)
Y
Y
Y
Y
Memory
Y
Pb
Pr
In memory, pixel values can be:
  Packed (i.e. interleaved)
  Sorted Pixels are grouped in memory by type
Cb
Cb
Cb
Cb
Cr
Cr
Cr
Cr
Video DAC
(e.g. Encoder)
We still haven't reduced the color info, yet ...

## Slide 26: Color (Chroma) Subsampling
Y
Y
Y
Y
Memory
Y
Pb
Pr
One way to reduce data would be to sample the color signals every other time
Variations of this scheme are used in many video systems
Cb
Cb
Cr
Cr
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y

## Slide 27: Color (Chroma) Subsampling
Y
Y
Y
Y
Memory
Y
Pb
Pr
One way to reduce data would be to sample the color signals every other time
Variations of this scheme are used in many video systems
This scheme is often referred to as 4:2:2 and is often represented as:
Cb
Cb
Cr
Cr
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y | Y
Y | Y
Cb | Cb
Cr | Cr

## Slide 28: Digital Video Formats (4:4:4, 4:2:2, 4:2:0, 4:1:1)
Y | Y
Y | Y
Cb | Cb
Y
Pb
Pr
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Cr | Cr
4:2:2
4:4:4 would be the original stream, with no chroma subsampling

## Slide 29: Digital Video Formats (4:4:4, 4:2:2, 4:2:0, 4:1:1)
Y | Y
Y | Y
Cb | Cb
Y
Pb
Pr
Cr | Cr
4:2:2
Y | Y
Y | Y
Y
Cb
Cr
Y
Y
Y
Y
Cb
Cr
Y
Y
Y
Y
Cb
Cr
Y
Y
Y
Y
Cb
Cr
Y
Y
Y
Y
Cb
Cr
Y
Y
Y
Y
Cb
Cr
Y
Y
Y
4:2:0
Cb
Cr
4:4:4 would be the original stream, with no chroma subsampling
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y

## Slide 30: Digital Video Formats (4:4:4, 4:2:2, 4:2:0, 4:1:1)
Y | Y
Y | Y
Cb | Cb
Y
Pb
Pr
Cr | Cr
4:2:2
Y | Y
Y | Y
4:2:0
Y | Y
Y | Y
Cb | Cr
Y
Cb
Cr
Y
Y
Y
Y
Cb
Cr
Y
Y
Y
Y
Cb
Cr
Y
Y
Y
4:1:1
Cb
Cr
4:4:4 would be the original stream, with no chroma subsampling
Y
Cb
Cr
Y
Y
Y
Y
Cb
Cr
Y
Y
Y
Y
Cb
Cr
Y
Y
Y
Y
Cb
Cr
Y
Y
Y
Y
Cb
Cr
Y
Y
Y
Y
Cb
Cr
Y
Y
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y
Y
Cb
Cr
Y

## Slide 31: Packed vs Sorted Pixels
Table 2-4. Pixel Interleaving Examples
Packing Format | Interleaved | Sequential | Separate
ABGR | ABGRABGR ABGRABGR ABGRABGR | AAABBBGGGRRR AAABBBGGGRRR | AAAAAAAA BBBBBBBBB GGGGGGGGG RRRRRRRRR
444 YCrCb, with CbYCr packing | CbYCrCbYCr CbYCr | CbCbCbYYYCrCrCr CbCbCbYYYCrCrCr | CbCbCbCbCbCb YYYYYY CrCrCrCrCrCr
420 YCrCb, with CbYCrY packing | CbYCrYYYCb YCrYYYCbY CrYYY | CbCbCbYYYYYYYYYYYYYCrCrCr CbCbCbYYYYYYYYYYYYCrCrCr | CbCbCbCbCbCb YYYYYYYYYYYY YYYYYYYYYYYY CrCrCrCrCrCr

## Slide 32: Summary: Pixel's in 4D
Dimensions:
Heigth
Width
Color Depth of the pixel
  How many bits are used to represent the color of each pixel?
1 bit
8 bits
Red: 8 bits
Green: 8 bits or YCbCr
Blue: 8 bits 4:2:2
width
h
Frame rate determines how long the pixel exists, i.e. how it moves

## Slide 33: Typical Video System Chain
Display
Capture
Process
Formatting Compression Encryption
Decryption Decompression
Video Input
NTSC/PAL
Decoder
Video Output
NTSC/PAL Encoder

## Slide 34: Typical Video System Chain
Formatting Compression Encryption
Decryption Decompression
Display
Capture
Process
Video Input
NTSC/PAL
Decoder
Video Output
NTSC/PAL Encoder
Process
Input
Decoder
Output
Encoder
Process
Store Transmit

## Slide 35: Video H/W Interfaces
Digital Data Format
Digital Hardware I/F
Encoder (Video DAC)
Analog Data Format
Analog Hardware I/F
Display / Monitor
Processing
Video Input
NTSC/PAL
Decoder
Video Output
NTSC/PAL Encoder

## Slide 36: Video H/W Interfaces
Digital Data Format
Digital Hardware I/F
Encoder (Video DAC)
Analog Data Format
Analog Hardware I/F
Display / Monitor
Analog Data Format
Analog Hardware I/F
Component
S-Video
CVBS
RF
Component
S-Video
CVBS
Processing
Video Input
Video Output

## Slide 37: Video Connections - RF
Radio Frequency (RF)
Coaxial Cable (RG58, RG59, RG6)
Off-the-Air (OTA) antenna
Audio/Video signals transmitted on RF carrier signal
Signals follow NTSC format in North America; PAL in Europe
Signals usually transmitted from attenna to TV via 75Ω coaxial cable
  Using RG58, RG59, or RG6 cable and F-connector
Luminance and color signals transmitted independently
  Historically, luminance information (Black/White/Gray) was introduced in the 1930's
  Color was added as a sideband signal later in the 1950's
Analog TV
Antenna (RF)

## Slide 38: Video Connections – Composite (CVBS)
Composite Video
VCR's provide two means of connecting to TV:
  RF – Tape playback "broadcast" on open channel (usually channel 3 or 4)
  Composite Video is one of three cables used to carry A/V line-level signals
    Composite video, also known as Composite Video with Blanking and Sync (CVBS), is a 75 ohm video cable using a Yellow RCA plug
    Right and Left audio channels using Red/White RCA plugs (respectively)
VCR recordings do not utilize the full NTSC resolution, rather they only achieve approximately SIF quality (~340x240)
CVBS improves performance by eliminating the RF carrier, and separating A & V
RF
or
Analog TV
VCR
CH 8
12:00
RF
COMP Video
Left
Right

## Slide 39: Video Connections: S-Video
S Video
S-Video
While most satellite receivers still have RF and CVBS cables, if an analog TV has an S-Video connection, it provides a noticable picture improvement
S-Video differs from composite (CVBS) by breaking out the video into two signals:
  Y – Luminance (black/white/gray)
  C – Chrominance (colors)
S-Video is provided by a circular jack with two differential signals (4 pins in jack)
Stereo audio is still provided by Left/Right RCA jacks
RG6
Analog TV
Digital Satellite
CH 8

## Slide 40: Video Connections: Component Video
New video sources (like DVD players) now incorporate Component Video outputs
Component differs from S-Video (Y/C) by further breaking out the chromo signal:
  Y – Luminance (black/white/gray)
  Pb – Chroma information (Luma – Blue)
  Pr – Chroma information (Luma – Red)
Y'Pb'Pr' specifies how data is physically sent to TV, not the data format. It can be sent in any format discussed earlier (480i, 480p, 720p, 1080i, etc.)
While some high-end products use BNC connectors, most Component outputs use three RCA plugs
Audio is (still) provided separately (will discuss later)
Digital TV
DVD
T2 CH3 10:53




Component Video
Y
Pr
Pb
Y
Pr
Pb

## Slide 41: Video H/W Interfaces
Digital Data Format
Digital Hardware I/F
Encoder (Video DAC)
Analog Data Format
Analog Hardware I/F
Display / Monitor
Video
DAC
(Encoder)
Processing
Video Input

## Slide 42: Video H/W Interfaces
Video
DAC
(Encoder)
Digital Data Format
Digital Hardware I/F
Encoder (Video DAC)
Analog Data Format
Analog Hardware I/F
Display / Monitor
YCbCr 4:2:2
BT.656 (shown later)
Processing
Video Input

## Slide 43: Output Summary
 | Video Processing | 
Analog Data Format |  | Digital Data Format
Digital Hardware I/F |  | Digital Hardware I/F
Decoder (Video ADC) |  | Encoder (Video DAC)
Analog Data Format |  | Analog Data Format
Analog Hardware I/F |  | Analog Hardware I/F
Analog Camera |  | Display / Monitor
Processing
Video Input
Decoder
Video Output
Encoder

## Slide 44: Input and Output
 | Video Processing | 
Digital Data Format |  | Digital Data Format
Digital Hardware I/F |  | Digital Hardware I/F
Decoder (Video ADC) |  | Encoder (Video DAC)
Analog Data Format |  | Analog Data Format
Analog Hardware I/F |  | Analog Hardware I/F
Analog Camera |  | Display / Monitor
Process
Input
Decoder
Output
Encoder

## Slide 45: What if it's a Digital Display?

## Slide 46: Digital Display (e.g. DTV, Computer)
 | Video Processing | 
Digital Data Format |  | Digital Data Format
Digital Hardware I/F |  | Digital Hardware I/F
Decoder (Video ADC) |  | 
Analog Data Format |  | 
Analog Hardware I/F |  | 
Analog Camera |  | Digital Display
Process
Input
Decoder
Output

## Slide 47: Digital Display (e.g. DTV, Computer)
 | Video Processing | 
Digital Data Format |  | Digital Data Format
Digital Hardware I/F |  | 
Decoder (Video ADC) |  | 
Analog Data Format |  | 
Analog Hardware I/F |  | 
Analog Camera |  | Digital Display
IEEE 1394
DVI
BT.656
BT.656 is a
very popular
chip-level interconnect
Process
Input
Decoder
Output

## Slide 48: Video Connections: DVI
The latest consumer video interface is the DVI (Digital Video Interface) connector.
While it is the first digital video I/F for the consumer market, many digital computer monitors use it as well. (It transfers 24-bit RGB or 24-bit YCbCr.)
DVI can be found in three variations:
  DVI-D – Digital signals (24 signals)
  DVI-A – Analog signals (5 analog signals similar to VGA: RGBHV)
  DVI-A/D – Analog and digital signals (24+5 = 29 signals)
Supports High-Bandwidth Digital Content Protection (HDCP) to ensure unauthorized copying of material is prevented
Audio is (still) provided separately (will discuss later)
Digital TV
HDTV Receiver
CH 38.1

## Slide 49: Digital Video Connections: IEEE 1394
High-speed, digital serial interconnect
  No need to convert digital data into analog and tolerate a loss of data integrity
  Physically small: Thin serial cable can replace larger and more expensive ones
  Easy to use: No need for terminators, device IDs, or elaborate setup
    6-pin connector provides power, 4-pin is very small
  Inexpensive: Priced for consumer products
  Scalable architecture:
    Supports 63 devices by daisy chaining and branching for true peer-to-peer comm.
    Hot pluggable: Add or remove 1394 devices with the bus active
    Cross platform: Apple (FireWire), Microsoft, HDTV, Sony (iLink), ect.
  Fast: Speeds of 100, 200, 400, and 800 Mbps
  Isochronous: Even real-time, multimedia data can be guaranteed its bandwidth for just-in-time delivery
DVD-Recorder
CH 8
2:43am
Digital TV
Notes: isochronous
Time-dependent. Pronounced eye-sock-ra-nuss, it refers to processes where data must be delivered within certain time constraints. For example, multimedia streams require an isochronous transport mechanism to ensure that data is delivered as fast as it is displayed and to ensure that the audio is synchronized with the video.
Isochronous can be contrasted with asynchronous, which refers to processes in which data streams can be broken by random intervals, and synchronous processes, in which data streams can be delivered only at specific intervals. Isochronous service is not as rigid as synchronous service, but not as lenient as asynchronous service.
Certain types of networks, such as ATM, are said to be isochronous because they can guarantee a specified throughput. Likewise, new bus architectures, such as IEEE 1394, support isochronous delivery.

## Slide 50: Video H/W Interfaces
 | Video Processing | 
Digital Data Format |  | Digital Data Format
Digital Hardware I/F |  | Digital Hardware I/F
Decoder (Video ADC) |  | Encoder (Video DAC)
Analog Data Format |  | Analog Data Format
Analog Hardware I/F |  | Analog Hardware I/F
Analog Camera |  | Display / Monitor
Process
Input
Decoder
Output

## Slide 51: Elements of a Video System
Analog Formats
Hardware Codecs
Software Codecs
Digital Formats
Formatting Compression Encryption
Decryption Decompression
Video Input
NTSC/PAL
Decoder
Video Output
NTSC/PAL Encoder

## Slide 52: You are entering…The Software Zone
Input
Decoder
Output
Encoder
Process
Store Transmit
Hardware
Software
Video Capture Device Driver
Store Transmit
Processing: Decryption
Decompression
Formatting
Etc.
Video Display Device Driver
Process
Processing: Formatting
Compression
Encryption
Etc.
Since Compression/Decompression is so important, let’s take a closer look at it.

## Slide 53: Why compression?
Video Capture Device Driver
Store Transmit
Decompression
Video Display Device Driver
Compression
Format 30 frames/s, 4:2:0 | Storage (90 min.) | Transmission
D1 (720x480) | 83.7 GBytes | ~15.5 Mbytes/s (124.4 Mbits/s)
CIF (352x288) | 23.3 GBytes | ~4.5 Mbytes/s (36.5 Mbits/s)
A movie won’t fit on a CD (800 MBytes) or a DVD (4.7 GBytes)
…and it can’t be streamed over ADSL (384 Kbits/s – 1.5Mbits/s) or common ethernet (10-100 Mbits/s)
Without it…

## Slide 54
Compression
Still Picture
MJPEG and MPEG
H.26x
H.264 (L) / MPEG 4-10
Windows Media Video9 (WMV9)
Others