## Slide 1
Analog Representations of Sound
Magnified phonograph grooves, viewed from above:
The shape of the grooves encodes the continuously varying audio signal.

## Slide 2
Analog to Digital Recording Chain
ADC
Continuously varying electrical energy is an analog of the sound pressure wave.
Microphone converts acoustic to electrical energy. It’s a transducer.
ADC (Analog to Digital Converter) converts analog to digital electrical signal.
Digital signal transmits binary numbers.
DAC (Digital to Analog Converter) converts digital signal in computer to analog for your headphones.

## Slide 3
Analog versus Digital
Analog
Continuous signal that mimics shape of acoustic sound pressure wave
Digital
Stream of discrete numbers that represent instantaneous amplitudes of analog signal, measured at equally spaced points in time.

## Slide 4
Analog to Digital Conversion
Instantaneous amplitudes of continuous analog signal, measured at equally spaced points in time.
A series of “snapshots”

## Slide 5
[a.k.a. “sample word length,” “bit depth”] Precision of numbers used for measurement: the more bits, the higher the resolution.
Example: 16 bit
Analog to Digital Overview
Sampling Rate
How often analog signal is measured
Sampling Resolution
[samples per second, Hz]
Example: 44,100 Hz

## Slide 6
Sampling Rate
Nyquist Theorem:
Sampling rate must be at least twice as high as the highest frequency you want to represent.
Determines the highest frequency that you can represent with a digital signal.
Capturing just the crest and trough of a sine wave will represent the wave exactly.

## Slide 7
Aliasing
What happens if sampling rate not high enough?
A high frequency signal
sampled at too low a rate
looks like …
… a lower frequency signal.
That’s called aliasing or foldover. An ADC has a low-pass anti-aliasing filter to prevent this.
Synthesis software can cause aliasing.

## Slide 8
Common Sampling Rates
Sampling Rate | Uses
44.1 kHz (44100) | CD, DAT
48 kHz (48000) | DAT, DV, DVD-Video
96 kHz (96000) | DVD-Audio
22.05 kHz (22050) | Old samplers
Most software can handle all these rates.
Which rates can represent the range of frequencies audible by (fresh) ears?

## Slide 9
3-bit Quantization
A 3-bit binary (base 2) number has 23 = 8 values.
0
1
2
3
4
5
6
7
A rough approximation
Amplitude
Time — measure amp. at each tick of sample clock

## Slide 10
4-bit Quantization
A 4-bit binary number has 24 = 16 values.
0
2
4
6
8
10
12
14
Amplitude
A better approximation
Time — measure amp. at each tick of sample clock

## Slide 11
Quantization Noise
Round-off error: difference between actual signal and quantization to integer values…
Random errors: sounds like low-amplitude noise

## Slide 12
The Digital Audio Stream
It’s just a series of sample numbers, to be interpreted as instantaneous amplitudes: one for every tick of the sample clock.
Previous example:
11 13 15 13 10 9 6 1 4 9 15 11 13 9
This is what appears in a sound file, along with a header that indicates the sampling rate, bit depth and other things.

## Slide 13
Common Sampling Resolutions
Word length | Uses
8-bit integer | Low-res web audio
16-bit integer | CD, DAT, DV, sound files
24-bit integer | DVD-Video, DVD-Audio
32-bit floating point | Software (usually only for internal representation)

## Slide 14
16-bit Sample Word Length
A 16-bit integer can represent 216, or 65,536, values (amplitude points).
We typically use signed 16-bit integers, and center the 65,536 values around 0.
32,767
-32,768
0

## Slide 15
Audio File Size
CD characteristics…
- Sampling rate:
44,100 samples per second (44.1 kHz)
How big is a 5-minute CD-quality sound file?
- Sample word length:
16 bits (i.e., 2 bytes) per sample
- Number of channels:
2 (stereo)

## Slide 16
Audio File Size
5 minutes * 60 seconds per minute
= 300 seconds
How big is a 5-minute CD-quality sound file?
44,100 samples * 2 bytes per sample * 2 channels
= 176,400 bytes per second
300 seconds * 176,400 bytes per second
= 52,920,000 bytes = c. 50.5 megabytes (MB)

## Slide 17
DAC: Sample and Hold
To reconstruct analog signal, hold each sample value for one clock tick; convert it to steady voltage.
0
1
2
3
4
5
6
7
Amplitude
Time

## Slide 18
DAC: Smoothing Filter
Apply an analog low-pass filter to the output of the sample-and-hold unit: averages “stair steps” into a smooth curve.
0
1
2
3
4
5
6
7
Amplitude
Time